## Slide 1
Emulating NXP S32K3X8EVB in QEMU & Porting FreeRTOS
CAOS Project Report
February 18th, 2025
Politecnico di Torino
Group 18 – Bertolami Carmelo, Frigo Matteo, Simoncini Marco, Soldera Marco
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)

## Slide 2
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)

## Slide 3
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
Introduction
Emulation S32K3X8EVB-Q289 in qemu
Can implementation
Uart Implementation
Porting freeRTOS
Develop an application
RX TX
CONTROLLER AREA NETWOEK

## Slide 4
Board Details
ARM Cortex-M7 CPU 32-bit architecture
Maximum frequency: up to 320 MHz
SoC S32K358
Designed for low energy consumption
especially in automotive applications

## Slide 5
QEMU Board
Emulation
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
Open-source emulator - Version: QEMU stable-8.2
Code Structure :
hw/arm/: Contains modules for ARM architectures and SoC management.
include/hw/: Header files and peripheral definitions.
target/arm/tcg/: CPU emulation, including Cortex-M7.
Modifications :
s32k358_soc.c - nxps32.c - Kconfig - Meson.build

## Slide 6
QEMU UART
Emulation
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
Supports transmission and reception of data.
UART (Universal Asynchronous Receiver-Transmitter) facilitates serial communication.
Implemented a driver for the SoC-specific UART in hw/char/.
DATA
CTRL
STAT
BAUD
REGISTERS:
Peripheral Emulation:

## Slide 7
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
CAN (Controller Area Network) is widely used in automotive applications.
Defines transmission and reception of frames.
Implemented FlexCAN controller in hw/net/can/ to support data transmission.
DATA
MCR
IFLAG1
IMASK1
REGISTERS:
ESR1
CTRL1
QEMU CAN
Emulation

## Slide 8
Compilation using NXP toolchain official IDE
Memory configuration replicated from the NXP linker file
FreeRTOS Porting
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
CPU configuration (vector table setup in QEMU)
Boot header removal to enable proper startup
HardFault fix by temporarily disabling the MPU

## Slide 9
FreeRTOS Porting:
Fixed memory mapping, boot_header, vector table.
MPU issues still unresolved needs further debugging.
Compilation & Configuration Issues:
Fixed Kconfig & meson.build for proper integration.
Main
Challenges
Board & SoC Adaptation:
Based on Netduino 2 adjusted memory, peripherals, addresses.
Peripheral Emulation:
UART: Adapted from Netduino 2.
CAN: No QEMU support for FlexCAN, built from scratch, complex bus synchronization.
Understanding & Adapting QEMU's Structure
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)

## Slide 10
Conclusion
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
Gained insights into hardware architecture and software implementation.
Accurate memory mapping was essential for reliable emulation.
Successfully implemented basic CAN and UART, overcoming protocol complexities.
Addressed memory configuration, vector table adjustments, and startup modifications.
Improved expertise in QEMU emulation, peripheral integration, and debugging.
Valuable experience for future embedded systems development.
Deeper Understanding of Hardware & Emulation :
Register Mapping & Peripheral Emulation :
FreeRTOS Porting Challenges :
Key Takeaways :

## Slide 11
Thank You
Group 18 – Bertolami Carmelo, Frigo Matteo, Simoncini Marco, Soldera Marco
© CAOS Group 18 2024/2025, licensed under CC BY-NC 4.0 (view slide 2)
Available for any question…